## Slide 1: Sterile Techniques- Surgical Hand Washing, Donning

## Slide 2: Preparation for scrubbing
Personal Hygiene
Shower
Healthy skin on hands, fingers, nails & arms.
No boil, abrasion or wound on hands
Free from cold or URTI

## Slide 3: Finger Nails
Short
Not over tips of fingers
Short nails
Easy to clean
Will not puncture gloves
Free from nail polish
Chipped nail polish can harbor bacteria
No artificial nails

## Slide 4: Jewelry
Remove all jewelry i.e. rings, watches, bracelets from hands & arms
Keep them at a sage place or in pocket
Dead skin & accumulate beneath them

## Slide 5: Theatre Attire
Scrub Suit
Surgical Cap & face mask
Eye Wear/Wiser
Shoes
Protective wearing
Plastic apron
Lead apron

## Slide 6: Scrub Suit
Street clothes not allowed
Short sleeved cotton scrub suit.
Sleeves 4 inches above elbow
Shirt tucked in trouser
-to avoid shirt tail flapping on sterile field
Trouser legs not touching floor
- to avoid transport of bacteria

## Slide 7: Shoes
Street shoes not allowed
Close ended shoes
Chappals or open ended shoes not allowed
Shoe cover for single use only

## Slide 8: Surgical Cap & Face mask
Surgical cap cover hair completely
Including pierced ear rings
Face mask cover nose & mouth completely

## Slide 9: Protective clothing
Lead apron if radiation exposure
Plastic apron in every case

## Slide 10: Areas Of The Operative Suite (Traffic Patterns)
Unrestricted- street clothes permitted
Semi-restricted- must have scrub attire & cap
Restricted-masks required

## Slide 11: Scrubbing Agents
Soap 5 minutes
Povidone iodine solution 2minutes ( 8ml required)
Chlor-hexidine Solution (Hibiclens) 2 minutes (8ml needed)

## Slide 12: Desirable properties of scrubbing agent
Non irritating to skin
Leaves minimum bacteria on skin
Prolonged antibacterial effect on skin
Should leather in hot, cold , or hard water

## Slide 13: Scrubbing Procedure
Nail brush for nails
Water Steady flow
Comfortable temperature.
Hands above the level of the elbows
Clothing should remain dry
Movements steady.

## Slide 14: Scrub technique
Scrubbing do not include rinsing time
Set water temperature
Wet hands & forearms
Hold soap in hands till scrubbing complete
Keep hands elevated above elbow through out

## Slide 15: Scrubbing Procedure
Turn off taps with elbows
Keep hands elevated.
Skin should be blotted dry
Use 2 towels
Towel should be folded
Discard towel immediately

## Slide 16: Gowning Procedure
Pick up gown from opened pack
gown is folded with the inside uppermost.
Slide both arms into gown
Not to touch outside the gown.
All gowns must be in a good state

## Slide 17: Parameters of a Sterile Gown
Gowns are considered sterile from waist level to chest level including sleeves to 2’ above elbow
Stockinette cuffs must be covered by sterile gloves
Sterile persons must have hands in sight at all times

## Slide 18: Gloving Procedure
The Open Method
Closed Method

## Slide 19
        Once gowned and gloved
stand with hand palms together
Above the waist
Away from the gown

## Slide 20: At the end of the sterile procedure
First remove the gown over the gloved hands
Then the gloves.
Hands should then be washed and dried.
Gloves disposed of according to policy

## Slide 21: Thank You