## Slide 1: Measurement of Oxygen Saturation Using Pulse Oximeter

## Slide 2: Oxygen Transport
Most of the oxygen in arterial blood is saturated on hemoglobin
Red blood cells must be adequate in number and have adequate hemoglobin
Sufficient circulation is necessary to transport oxygen to the cellular level

## Slide 3: Oxygen Saturation
Percentage of hemoglobin saturated with oxygen
Normal SpO2 is 95-98%
Suspect cellular perfusion compromise if less than 95% SpO2
  Insure adequate airway
  Provide supplemental oxygen
  Monitor carefully for further changes and intervene appropriately

## Slide 4: continued
Suspect severe cellular perfusion compromise when SpO2 is less than 90%
  Insure airway and provide positive ventilations if necessary
  Administer high flow oxygen
  Head injured patients should never drop below 90% SpO2

## Slide 5: SpO2 and PaO2
SpO2 indicates the oxygen bound to hemoglobin
  Closely corresponds to SaO2 measured in laboratory tests
  SpO2 indicates the saturation was obtained with non-invasive oximetry
PaO2 indicates the oxygen dissolved in the plasma
  Measured in ABGs

## Slide 6: continued
Normal PaO2 is 80-100 mmHg
  Normally
    80-100 mm Hg corresponds to 95-100% SpO2
    60 mm Hg corresponds to 90% SpO2
    40 mm Hg corresponds to 75% SpO2

## Slide 7: Technology
The pulse oximeter has Light-emitting diodes (LEDs) that produce red and infrared light
LEDs and the detector are on opposite sides of the sensor
Sensor must be place so light passes through a capillary bed
  Requires physiological pulsatile waves to measure saturation
  Requires a pulse or a pulse wave (Adequate CPR)

## Slide 8: continued
Oxygenated blood and deoxygenated blood absorb different light sources
  Oxyhemoglobin absorbs more infrared light
  Reduced hemoglobin absorbs more red light
  Pulse oximetry reveals arterial saturation my measuring the difference.

## Slide 9: Patient Assessment
Patient assessment should include all components
  Scene Size-up
  Initial Assessment
  Rapid Trauma Assessment or Focused Physical Exam
  Focused History
  Vital Signs
  Detailed Assessment
  Ongoing Assessment

## Slide 10: Pulse Oximetry Monitoring
Pulse oximetry monitoring is NOT intended to replace any part of the patient assessment
  Pulse oximetry is a useful adjunct in assessing the patient’s oxygenation and monitoring treatment interventions
Initiate pulse oximetry immediately prior to or concurrently with oxygen administration

## Slide 11: Continuous Monitoring
Monitor current oxygenation status and response to oxygen therapy
Monitor response to nebulized treatments
Monitor patient following intubation
Monitor patient following positioning patients for stabilization and transport
Decreased circulating oxygen in the blood may occur rapidly without immediate clinical signs and symptoms

## Slide 12: Pediatrics
Use appropriate sized sensors
  Adult sensors may be used on arms or feet
Active movement may cause erroneous readings
  Pulse rate on the oximeter must coincide with palpated pulse
Poor perfusion will cause erroneous readings
  Treat patient according to clinical status when in doubt
  Pulse oximetry is useless in pediatric cardiac arrest

## Slide 13: Conditions Affecting Accuracy
Patient conditions
  Carboxyhemoglobin
  Anemia
  Hypovolemia/Hypotension
  Hypothermia

## Slide 14: Carboxyhemoglobin
Carbon monoxide has 200-250 greater affinity for the hemoglobin molecule than oxygen
  Binds at the oxygen binding site
  Prevents on-loading of oxygen
  Fails of readily off-load at the tissue cells
Carboxyhemoglobin can not be distinguished from oxyhemoglobin by pulse oximetry
  Erroneously high reading may present

## Slide 15: continued
Suspect the presence of carboxyhemoglobin in patient with:
  Smoke inhalation
  Intentional and accidental CO poisoning
  Heavy cigarette smoking
Treat carboxyhemoglobin with high flow oxygen irregardless of the pulse oximetry reading!

## Slide 16: Anemia
Low quantities of erythrocytes or hemoglobin
  Normal value of hemoglobin is 11-18 g/dl
  Values as low as 5 g/dl may result in 100% SpO2
Anemic patients require high levels of oxygen to compensate for low oxygen carrying capacities!

## Slide 17: Hypovolemia/Hypotension
Adequate oxygen saturation but reduced oxygen carrying capacity
Vasoconstriction or reduction in cardiac output may result in loss of detectable pulsatile waveform at sensor site
Patients in shock or receiving vasoconstrictors may not have adequate perfusion to be detected by oximetry
Always administer oxygen to patients with poor perfusion!

## Slide 18: Hypothermia
Severe peripheral vasoconstriction may prevent oximetry detection
Shivering may result in erroneous oximetry motion
  Pulse rate on oximeter must coincide with palpable pulse rate to be considered accurate
  Treat the patient according to hypothermic guidelines and administer oxygen accordingly!

## Slide 19: Patient Environments
Ambient Light
Excessive Motion

## Slide 20: Ambient Lighting
Any external light exposure to capillary bed where sampling is occurring may result in an erroneous reading
Most sensors are designed to prevent light from passing through the shell
  Shielding the sensor by covering the extremity is acceptable

## Slide 21: Excessive Motion
New technology filters out most motion artifact
Always compare the palpable pulse rate with the pulse rate indicated on the pulse oximetry
  If they do not coincide, reading must be considered inaccurate

## Slide 22: Other Concerns
Fingernail polish and pressed on nails
  Most commonly use nails and fingernail polish will not affect pulse oximetry accuracy
  Some shades of blue, black and green may affect accuracy (remove with acetone pad)
  Metallic flaked polish should be removed with acetone pad
  The sensor may be placed on the ear if reading is affected

## Slide 23: continued
Skin pigmentation
  Apply sensor to the fingertips of darkly pigmented patients.

## Slide 24: Interpreting Pulse Oximetry
Assess and treat the PATIENT not the oximeter!
  Use oximetry as an adjunct to patient assessment and treatment evaluation
  NEVER withhold oxygen if the patient ahs signs or symptoms of hypoxia or hypoxemia irregardless of oximetry readings!

## Slide 25: continued
Pulse oximetry measures oxygenation not ventilation
  Pulse oximetry does NOT indicate the removal of carbon dioxide from the blood!

## Slide 26: Documentation
Pulse oximetry is usually documented as SpO2
  Distinguishes non-invasive pulse oximetry from SaO2 determined by laboratory testing
Document oximetry readings as frequently as other vital signs
When oximetry reading is obtained before oxygen administration, designate the reading as “room air”

## Slide 27: continued
When oxygen administration is changed, document the evaluation of pulse oximetry
When treatments provided could potentially affect respiration or ventilation, document pulse oximetry
  Spinal immobilization
  Shock position
  Fluid administration

## Slide 28: Summary
As with all monitoring devices, the interpretation of information and response to that interpretation is the responsibility of a properly trained technician!

## Slide 29: Thank You