## Slide 1: Nebulization

## Slide 2: Using a Nebulizer
Many medications are available as inhaled treatments. Inhaled methods deliver medication directly to the airway, which is helpful for lung diseases. The patient and health care provider can choose from a variety of delivery systems for inhaling medication.
A nebulizer delivery system consists of a nebulizer (small plastic bowl with a screw-top lid) and a source for compressed air. The air flow to the nebulizer changes the medication solution to a mist. When inhaled correctly, the medication has a better chance to reach the small airways. This increases the medication's effectiveness.

## Slide 3: How to Assemble the Nebulizer and Air Compressor
Place the compressor where it can safely reach its power source and where you can reach the ON/OFF switch.
Wash your hands prior to preparing each treatment.
Use a clean nebulizer.
Measure the correct dose of medication and other solutions prescribed by your physician. Add these to the nebulizer.
Connect the air tubing from the compressor to the nebulizer base.
Attach a mouthpiece to the nebulizer.

## Slide 4
Turn the compressor on and check the nebulizer for misting. When using a finger valve, cover the air hole to force the air to the nebulizer.
If the Nebulizer Is Not Misting
      Check all connections.
      Refer to manufacturer's instructions

## Slide 5: Taking the Nebulized Treatment
Put the mouthpiece in your mouth between teeth and close lips around it.
Hold the nebulizer in an upright position. This prevents spilling and promotes nebulization.
Assure deep breathing throughout the treatment. This allows the medication time to deposit in the airway.
Occasionally tapping the side of the nebulizer helps the solution drop to where it can be misted.
Continue these steps until the onset of inconsistent nebulization.

## Slide 6: Care and Cleaning of Nebulizer Equipment After Each Use
Please follow the manufacturer’s instructions for cleaning the nebulizer equipment. Some suggested guidelines include the following:
Take apart the nebulizer. Wash all parts (except tubing and finger valve) in liquid dish soap and water. Rinse with water.
After washing the nebulizer shake off any excess water.
Reattach the nebulizer pieces and tubing to the air compressor and turn on the compressor to dry the nebulizer quickly. Make sure the nebulizer is completely dry before storing the nebulizer.

## Slide 7: Care and Cleaning of Nebulizer Equipment Every Other Treatment Day
There are two ways to disinfect and sterilize nebulizer.
Boiling the nebulizer is the preferred method if nebulizer can be boiled.

## Slide 8: Boiling Water
Wash your hands.
Take the nebulizer apart.
Put all the parts except the mask, tubing and interrupter in boiling water for 10 minutes.
After boiling the nebulizer shake off any excess water
Reattach the nebulizer pieces and tubing to the air compressor and turn on the compressor to dry the nebulizer quickly. Make sure the nebulizer is completely dry before storing the nebulizer.

## Slide 9: Vinegar and Water
Wash your hands.
Soak all parts of the nebulizer (except mask, tubing and interrupter) for 1 hour in a solution of 1 part distilled white vinegar and 3 parts hot water. The solution should be fresh. Remove the parts from the vinegar solution and rinse them in water. Discard the solution.
Shake off any excess water.
Reattach the nebulizer pieces and tubing to the air compressor and turn on the compressor to dry the nebulizer quickly. Make sure the nebulizer is completely dry before storing the nebulizer.

## Slide 10
The tubing is replaced every two weeks because it is difficult to clean and dry properly.

## Slide 11: Care of the Compressor
Check the manufacturer's instructions for cleaning and care of the compressor.

## Slide 12: Thank You